Advantech SE Technical Share Document

| Date | 2019 / 4 / 2 | SR# | 0007 |
| --- | --- | --- | --- |
| Category | □ FAQ■ SOP | Related OS | RTOS / WINCE / Windows |
| Abstract | How to connect HMI and Keyence_KV7000 via Ethernet |
| Keyword | WOP-2000 / WA-HT3000 / WebAccess/HMI Runtime Keyence KV7000 |
| Related Product |  |
| Author |  |

- Problem Description:

How to connect HMI and Keyence_KV7000 via Ethernet

- Brief Solution - Step by Step:

Keyence KV7000 Ethernet

The introduction is how to connect Keyence KV 7000 series with WebAccess/HMI and takes KV-7000 Ethernet connection as an example.

1. Keyence KV7000 PLC setting

Set IP Address

KV software path: start => program files => KEYENCE => KV STUDIO Ver.6

Detect KV PLC IP

Monitor/Simulator (N) => Setup communication => setup communication

Read from PLC

PLC Parameter Setting

Write parameter setting to PLC

2. HMI Setting

Choose Device/Server Setting: Keyence Corp. ( KV-7000

Parameter Setting: Default Port is ”8501”

PLC Device List

Bit Devices

Word Devices

- Reference: