Advantech SE Technical Share Document

| Date | 2019 / 04 / 30 | SR# | 0008 |
| --- | --- | --- | --- |
| Category | □ FAQ■ SOP | Related OS | RTOS / WINCE / Windows |
| Abstract | How to connect HMI and MITSUBISHI FX5U-32M via RS-485 port |
| Keyword | WOP-2000 / WA-HT3000 / WebAccess/HMI Runtime FX5U |
| Related Product | WOP-2000, WA-HT3000, WebAccess/HMi Runtime |
| Author |  |

- Problem Description:

How to connect HMI and MITSUBISHI FX5U-32M via RS-485 port

- Brief Solution - Step by Step:

MITSUBISHI FX5U-32M PLC

此技術檔是說明WebAccess/HMI與MITSUBISHI FX5U-32M PLC COM port之設定。

PLC軟體連線及參數設定:

使用網路線將PC與FX5U PLC連接。

步驟一: 打開GX WORKS3軟體，新建工程，選擇FX5CPU，機型選擇FX5U。

步驟二: 選擇【線上】->【連接目標指定】，如圖1所示:

圖1

步驟三: 進入連接設置介面（圖2），按兩下選擇【Ethernet Board】連接，按兩下【PLC Module】設置與電腦連接方式（圖3）:

圖2

圖3

步驟四：選擇【乙太網埠直接連接】直接連接或【經由集線器連接】經過交換機連接，點擊搜索會顯示連接到到前PC的PLC及IP地址。

設置完成後點擊確定回到連接目標指定介面，點擊通訊測試，會提示“已成功與FX5UCPU連接”。

步驟五：設定通訊協議格式。

在【導航】裡選擇【參數】->【FX5UCPU】(【模組參數】(【485串口】，參數設置如圖4：

MC協議,19200，7，奇，1，和校驗，站號0，格式4

注：串列傳輸速率可根據需要自行調整。

圖4

步驟六：設置完成後，轉換程式並寫入PLC中（圖5）：

圖5

步驟七：寫入完成後需RESET或重新將PLC上電。

HMI 參數設定:

步驟八：驅動選擇【直接連接（串口）】->【Mitsubishi Electric Corp.-> Melsec-FX5U-32M】

設定HMI連接參數（圖6）：

圖6

步驟九：HMI連接1參數與PLC 參數設定為相同（圖7）：

圖7

PLC 記憶體位址

Bit Device:

Word Device:

接線圖:

- Reference: