Subject: How to install ISA bus ICOM card under Windows system?

Prepared by : kuei.Chen

| 1.0 | Description | This video is to show you how to install ISA bus ICOM card under Windows system. |
| --- | --- | --- |
| 2.0 | Product(s) | All ISA bus communication card. PCL-740, PCL-741, PCL-742, PCL-743S, PCL-745S, PCL-746, PCL-841, PCL-846, PCL-847, PCL-849, PCL-849L, PCL-858, PCM-3610, PCM-3612, PCM-3614, PCM-3618, PCM-3640, PCM-3641, PCM-3680 |
| 3.0 | System requirement | OS | Windows 98/ 2000/ XP |
|  |  | Hardware | Host PC (X86 motherboard with ISA bus slot), ISA bus communication card |
|  |  | Software | ISA configuration tool, ADAM-4000-5000 Utility |
| 4.0 | System architecture and configuration |  |
| 5.0 | Operating Procedures | 1. Set Hardware switch setting for I/O address and IRQ number 2. Execute ISA Configure tool to registry these setting 3. Check new COM ports from Windows Device Manager 4. Test these new COM ports via Utility |

# Text boxes

Host PC

ISA configuration tool

ISA bus slot

ISA bus communication card