Product:

EKI Managed Switches

Abstract:

X-Ring limitation of Coupling Ring Topology

Description:

User should take those limitations into consideration while developing their network architecture using X-Ring Coupling Ring topology.

Solution:

X-Ring Coupling Ring Limitation 1: The connection between control ports of each X-ring group must always be active.

In couple ring, the network connection between the control ports must always be steady. So, in case of physical connection issue occurred in the primary path, the link-down message may always be send to backup path switch via control port, which allows the backup path to takes over as the active route.

X-Ring Coupling Ring Limitation 2: X-Ring support only allow to group up to 2 X-Ring groups to form a coupling ring for redundant backup.

In couple ring topology network, users can only group up to 2 X-Ring groups to form a coupling ring for redundant backup.

X-Ring Coupling Ring Limitation 3: Coupling Ring switch can not be the X-Ring Master switch

In couple ring topology, the switches to be configured as members of the Coupling Ring group cannot be the X-Ring Master device of their X-ring group.