Product:

EKI Managed Switches

Abstract:

X-Ring limitation of Dual-Homing Topology

Description:

User should take those limitations into consideration while developing their network architecture using X-Ring Dual-Homing topology.

Solution:

X-Ring Dual-Homing Limitation 1: X-Ring support up to 2 Dual-Homing sub rings ONLY.

X-Ring Dual-Homing Limitation 2: Dual-Homing switch cannot be the X-Ring Master switch

When set up one of port on the switch to be the Dual-Homing port, the switch can NOT be configured as Ring Master Switch within the X-Ring group. Enable Ring Master on other switches within X-Ring group instead the Dual-Homing switch.