Advantech AE Technical Share Document

| Date | 2015 / 04 / 07 | SR# |  |
| --- | --- | --- | --- |
| Category | ■ FAQ □ SOP | Related OS | RTOS |
| Abstract | How to use VNC for WebOP-2000T |
| Keyword | VNC/ WOP/ WebOP |
| Related Product | WOP-2000T Series |

- Problem Description:

How to use VNC for WebOP-2000T

- Brief Solution - Step by Step:

- Please download VNC Viewer software to your computer in advance.

http://www.realvnc.com/download/viewer/

- Please enter Panel Setup Screen and touch FTP/VNC button.

- Make sure if VNC is enabled.

- Click OK.

- Run VNC Viewer and enter IP address of WebOP

- Click Continue

- The default password of WebOP is 9 digit of ‘0’

- Reference:

N/A