Advantech AE Technical Share Document

| Date | 2015 / 04 / 08 | SR# |  |
| --- | --- | --- | --- |
| Category | ■ FAQ □ SOP | Related OS | RTOS |
| Abstract | How to Save file in USB disk and get it from FTP remotely |
| Keyword | WOP/ WebOP/ FTP/ Data Logger/ Save File |
| Related Product | WOP-2000V Series/ WOP-2000T Series |

- Problem Description:

How to Save file in USB disk and get it from FTP remotely

- Brief Solution - Step by Step:

System Diagram

- Create new project.

- Select the model of your panel HMI.

- Select protocol of your device / controller.  For example, we use Modbus RTU driver.

- Setup communication parameter according to your device / controller.

- Right-click on Data Logger and click Add Data Logger.

- For example here, we will read Modbus Address 40001 ~ 40003 every one second.  And the data will be saved into E:\DeviceData.csv every 5 minutes.

(WOP-2000T Series -  	C: - Local Disk / D: MicroSD Card / E: USB Hard Disk)

(WOP-2000V Series - 	D: USB Hard Disk)

So in this case, we will save data into USB Hard Disk.

- Enter Panel Setup Mode of WOP-2000.

- Click FTP/VNC button and set FTP server path as E:\.  As we mentioned E: is USB hard disk for WOP-2000T series.  So FTP user will find the files under USB during login remotely.  In other hand, you might able to change to C: and user could access file from local flash memory of WOP-2000T.

- Login by 3-party FTP client tool:

Default Account	:  user

Password			:  88888888 (for level 8 user)

The password will depends on Panel Setup – FTP/VNC Setting.

- Reference:

N/A