Please confirm what wiring the user’s motor driver uses.

If user’s wiring is like it as below described in manual.

It is equal to it as below.

The EXT.VCC is the pull-high circuit for OUT/DIR.

So if user wants to use the PCI-1243 instead of 839.

PCI-1243 doesn’t provide the internal pull-high circuit. (Only provide the open-collect)

So user has to make the pull-high circuit in the external.

Just like it as below.

Please make sure the max current sink the driver allowed to decide how big the pull-high resister is.