Advantech AE Technical Sharing Documentation

| Date | 2017 / 10 / 24 | SR# | 1-3049670511 |
| --- | --- | --- | --- |
| Category | ■ FAQ □ SOP | Related OS | WIN7 |
| Abstract | How to use SUSI converter to implemnt with RMM Agent |
| Keyword | SUSI converter / RMM / EC lmsensor |
| Related Product | UNO series |

- Problem Description:

Users can implement SUSI convertor for RMM server to read necessary hardware information. SUSI convertor is included within the latest embedded image.

- Brief Solution - Step by Step:

Step1

Remove the old version of EC related drivers. For example, drivers shown below needs to be removed.

Step2

Install the latest EC driver found from the support portal.

http://support.advantech.com/Support/DownloadSRDetail_New.aspx?SR_ID=1-R5OARM&Doc_Source=Download

Step3

Install the latest SUSI convertor, installation method is included in the ZIP file.

http://support.advantech.com/Support/DownloadSRDetail_New.aspx?SR_ID=1-1EB94YS&Doc_Source=Download

Step4

Install the SNMP subagent to install necessaty components.

http://support.advantech.com/Support/DownloadSRDetail_New.aspx?SR_ID=1-W6XUPF&Doc_Source=Download

Step5

Once finished the above steps, reboot the system.

Step6

Install the SusiIOT provided by RMM team.

http://support.advantech.com/Support/DownloadSRDetail_New.aspx?SR_ID=1-1EB94YS&Doc_Source=Download

Step7

Once installing the agent suggested from their website.

http://support.advantech.com/Support/DownloadSRDetail_New.aspx?SR_ID=1-16GHUTP&Doc_Source=Download

You should be able to read the hardware information from RMM server.

- Reference:

Advantech-IPS

http://www.advantech.tw/products/1-2mlj2z/uno-ips2730-ae/mod_2ca60cb5-a216-4f76-accb-4c3108e8621e