| Subject 主題: How to get the list of supporting examples for DA&C cards? |
| --- |
| Prepared by :Kurt Chen 製作者 | Verify by: 校對者 | Confirmed by: |
| Filename of video影像檔名: | Location 所在位置: |

| 1.0 | Description 主旨說明 | This Demo video shows how to get the list of supporting examples for DA&C cards. |
| --- | --- | --- |
| 2.0 | Product(s) 適用對象 | All Advantech DA&C cards. PCI-1710/ 1710L/1710HG/1710HGL, PCI-1711/1711L, PCI-1712/1712L, PCI-1716/1716L, PCI-1718HDU, PCI-1718HGU, PCL-1718HD/HG, PCI-1714U, PCI-1742U, PCL-711B, PCL-812PG, PCL-818L, PCI-1713, PCI-1714, PCI-1714UL, PCI-1747U, PCI-1715U, PCL-813B, PCI-1720U, PCI-1721, PCI-1723, PCI-1724U, PCI-1727U, PCL-727, PCL-726, PCL-728, PCI-1751U, PCI-1753, PCI-1753E, PCI-1755, PCI-1735U, PCL-720+, PCI-1737U, PCL-724, PCI-1739U, PCL-731, PCI-1757UP, PCL-722, PCI-1730, PCL-730, PCI-1733, PCL-733, PCI-1734, PCL-734, PCI-1750, PCI-1752, PCI-1754, PCI-1756, PCI-1758UDI, PCI-1758UDO, PCI-1758UDIO, PCI-1736UP, PCI-1763UP, PCI-1761, PCL-725, PCI-1760U, PCI-1762, PCL-735, PCL-836, PCI-1780, PCM-3712, PCM-3718H/HG/HO, PCM-3724, PCM-3725, PCM-3730, PCM-3780, USB-4711, USB-4716, USB-4718, USB-4751, USB-4761, USB-4671 |
| 3.0 | System requirement 系統需求 | OS | Windows XP/ 2000/ 98/ 95/ NT |
|  |  | Hardware | Host PC, DA&C card |
|  |  | Software | Advantech Device Manager, 32-bit DLL driver |
| 4.0 | System architecture and configuration 系統架構與設定 | DA&C cards Advantech Device Manager DLL driver for DA&C cards |
| 5.0 | Preventive Action 操作步驟 | Install device manager Install DLL driver Open software manual Find examples of PCI-1710 Find examples of PCL-711 |