| Subject 主題: How to log data of ADAM-4118 through OPC server and DLL driver in ADAMVIew |
| --- |
| Prepared by : Shaoyi Wang 製作者 | Verified by: 校對者 | Confirmed by: |
| Filename of video影像檔名: | Location 所在位置: |

| 1.0 | Description 主旨說明 | This user guide is to show you how to log data of ADAM-4118 through OPC server and DLL driver in ADAMVIew. |
| --- | --- | --- |
| 2.0 | Product(s) 適用對象 | All ADAM-4000 series modules and ADAM-5000/485 plus ADAM-5000 series modules which use ADAMView as human-machine-interface software. |
| 3.0 | System requirement 系統需求 | OS | Windows 98/ XP/ 2000/ NT 4.0 or higher |
|  |  | Hardware | Host PC, ADAM-4118, ADAM-4520, RS-232 direct cable, RS-485 twisted wires |
|  |  | Software | ADAMView, ADAM OPC Server, ADAM DLL driver, Advantech device manager |
| 4.0 | System architecture and configuration 系統架構與設定 |  |
| 5.0 | Preventive Action 操作步驟 | Connect the hardware as the above diagram shows. Set the ADAM OPC Server and read the CH0 value of ADAM-4118 from the OPC Server. Set the Advantech Device Manager and read the CH0 value of ADAM-4118 from Device Manager. Log the data in the hard disk. |

# Text boxes

Ch0 input

RS-232

DATA+

ADAM-4118

DATA-

Host PC

ADAMView

ADAM-4520