| Subject 主題: How to send ASCII commands to ADAM-4000 series modules and ADAM-5000 series with ADAM-5000/485 modules. |
| --- |
| Prepared by : Shaoyi Wang 製作者 | Verified by: 校對者 | Confirmed by: |
| Filename of video影像檔名: | Location 所在位置: |

| 1.0 | Description 主旨說明 | This user guide shows how to send ASCII commands to ADAM-4000 series modules and ADAM-5000 series with ADAM-5000/485 modules through the “Microsoft Visual Basic” program. |
| --- | --- | --- |
| 2.0 | Product(s) 適用對象 | All ADAM-4000 and ADAM-5000/485 series modules with Advantech protocol. ADAM-4011/4011D, ADAM-4012, ADAM-4013, ADAM-4015, ADAM-4015T, ADAM-4016, ADAM-4017/4017+, ADAM-4018/4018+, ADAM-4019+, ADAM-4021, ADAM-4022T, ADAM-4024, ADAM-4050, ADAM-4051, ADAM-4052, ADAM-4053, ADAM-4055, ADAM-4056S/ 4056SO, ADAM-4060, ADAM-4068, ADAM-4069, ADAM-4080/4080D, ADAM-4117, ADAM-4118, ADAM-4150, ADAM-4168, ADAM-5013, ADAM-5017, ADAM-5017UH, ADAM-5018, ADAM-5018P, ADAM-5024, ADAM-5050, ADAM-5051/5051D, ADAM-5051S, ADAM-5052, ADAM-5055S, ADAM-5056/5056D, ADAM-5056S/5056SO, ADAM-5060/5068, ADAM-5069, ADAM-5080. |
| 3.0 | System Requirements 系統需求 | OS | Windows XP/ 2000 |
|  |  | Hardware | ADAM-4520, ADAM-4118, RS-232, RS-485, Thermocouple (or other input device corresponding to different modules) |
|  |  | Software | ADAM-4000-5000 Utility, Microsoft Visual Basic |
| 4.0 | System Architecture & Configuration 系統架構與設定 |  |
| 5.0 | Preventive Action 操作步驟 | Connect the wiring as the above diagram shows. Launch ADAM utility to connect with ADAM-4000 module. Send ASCII command manually in the terminal mode of utility. Please refer to the video file 4118_terminal. A tutorial film also demonstrates how to send ASCII command via VB 6.0 4118_vb. |
| Appendix | Utility and user manual: Download and install the utility in the path: http://www.advantech.com.tw/support/sr_detail.asp?SR_ID=1%2D9HOC2 The user manual is in the path: http://www.advantech.com.tw/support/sr_detail.asp?SR_ID=1%2BGE%2B715 |

# Text boxes

Ch0 input

DATA+

DATA-

ADAM-4118

ADAM-4520

(Host PC)

ADAM-4000-5000 Utility

VB program

RS-232