Subject : How to get Modbus data from ADAM-4572

Prepared by : kuei.Chen

| 1.0 | Description | This video is to show you how to get Modbus data from ADAM-4572. |
| --- | --- | --- |
| 2.0 | Product(s) | Popular HMI software with Modbus/TCP driver or OPC server ADAM-4015, ADAM-4015T, ADAM-4017+, ADAM-4018+, ADAM-4019+, ADAM-4024, ADAM-4051, ADAM-4055, ADAM-4068, ADAM-4069, ADAM-4117, ADAM-4118, ADAM-4150, ADAM-4168, ADAM-5000/485, ADAM-5000E, ADAM-5511 |
| 3.0 | System requirement | OS | Windows 98/ 2000/ XP |
|  |  | Hardware | Host PC, ADAM-4017+, ADAM-4572, LAN cable, RS-485 two twisted wires |
|  |  | Software | EDG Configuration Utility, Advantech Modbus TCP OPC server |
| 4.0 | System architecture and configuration |  |
| 5.0 | Operating Procedure | Connect devices as above diagram shows. Set ADAM-4572 Network Configuration in Utility Set Modbus Configuration parameter in Utility Run Advantech Modbus TCP OPC Server in Windows Host PC Monitor Modbus data |

# Text boxes

DATA-

DATA+

ADAM-4017+

RS-485

LAN Cable

ADAM-4572

Host PC

EDG Configuration Utility

Advantech Modbus TCP OPC server