Title How can transfer data from RS-485 to RS-422? Product Model : ADAM-4520, ADAM-4510I Type : Knowledge Base – FAQ Abstract : How can transfer data from RS-485 to RS-422? Description : If user wants to transfer data from RS-485 type to RS-422 type, what kind of module should be used? And how to connect them? Category : Programming Operating System :

Solution

There are two connecting methods, one is using an ADAM-4510I, and the other is using two ADAM-4520. The connecting figures are as follows. 1. Using an ADAM-4510I, but it is 2. Using 2 ADAM-4520

# Text boxes

Host PC

ADAM- 4510I

422 device

RS-485

RS-422

RS-422

RS-485

422 device

ADAM- 4520

Host PC

ADAM- 4520

Half-duplex

RS-232