Products:

UNO-2172, UNO-2182, UNO-3282

Abstract:

Boot from LAN function can’t work

Description:

Some users set the 1st boot device as LAN but found UNO can’t boot from LAN.

Solution:

Following is memory mapping when system power on. The device ROMs will be loaded at 769KB~896KB. (Only 128KB)

In the UNO system, LAN boot rom, USB legacy device, SRAM device will be allocated at this memory space during POST stage. Due to the limited memory space, not all the devices can be allocated successful.

In this case, if the SRAM function is not necessary, suggest disabling SRAM device then upper memory can release some memory to load the LAN boot rom.

END