Access data from ADAM-6000 series via internet :

If want to access data from ADAM-6000 series via internet , there is one point important and must know , ADAM-6000 series modules only allow 8 connections , it means 8 host computers can access data at the same time , if access data via internet , because the communication quality is not 100 % good , so the connection will not always success , if failure , the connection on ADAM-6000 series will not be released immediately , it will be released after TCP/IP timeout , the default timeout is more then 12 minutes , and if communication failure over 8 times , then you won’t connect to modules anymore before timeout , you must wait for the ADAM-6000 release one connection .

The solution is we can set the host idle time in utility , the module will detect the connection is under communicating or not , if not , then over the host idle time , module will release the connection automatically .