Advantech AE Technical Share Document

| Date | 2015 / 04 / 07 | SR# |  |
| --- | --- | --- | --- |
| Category | ■ FAQ □ SOP | Related OS | Win7/ WinXP |
| Abstract | How to enable Trigger Bit in Data Logger |
| Keyword | WOP/ WebOP/ Trigger/ Data Logger |
| Related Product | WOP-2000V/ WOP-2000T/ WOP-3000T/ Panel Express |

- Problem Description:

How to enable Trigger Bit in Data Logger

- Brief Solution - Step by Step:

Double click on Command & Status

Tick “Use Command Block” and set an address(internal register U500 for example), select 4 words.  Then, click tag “Command Block”

Tick “Trigger Bits #0 - #15”.  $C3 = $U503 because we set address U500 in previous page.

Add new data logger.

The trigger bit would be enabled in data logger. For example in this case if we select #0. Once $U503.0 switched to ON (OFF ( ON ), the value of internal register U300 will be record.

- Reference:

N/A